Chapter 7

1. Walker3 7.P.047. [549629] Show Details A candy bar has a mass of 0.048 kg and a calorie rating of 205 Cal. What speed would this candy bar have if its kinetic energy were equal to its metabolic energy. [Note: The nutritional calorie, 1 Cal, is equivalent to 1000 calories (1000 cal) as defined in physics. In addition, the conversion factor between calories and joules is as follows: 1 Cal = 1000 cal = 1 kcal = 4186 J.] 5.98 km/s

[Answer]

Kinetic energy of the candy bar = 205 * 4186 J = 1/2 m v2

Therefore, it’s velocity v = sqrt ( 2*205*4186/0.048) = 5.98e3 m/s = 5.98 km/s

2. Walker3 7.P.049. [549594] Show Details You push a 40 kg box across a floor where the coefficient of kinetic friction is µk = 0.55. The force you exert is horizontal. (a) How much power is needed to push the box at a speed of 0.70 m/s? 151 W (b) How much work do you do if you push the box for 44 s? 6.64 kJ

[Answer]

(a) Power = Force dot_product velocity

Force = Friction force = N * µk = mg *µk= 40 * 9.81 * 0.55 N

Thus, power

P = Force * speed * cos (angle between force and velocity)

= 40*9.81*0.55*0.70 = 151 W

(b) W = P * Δt = 151 W * 44s = 6.64 kJ

3. Walker3 7.P.052. [549620] Show Details After a tornado, a 0.60 g straw was found embedded 2.7 cm into the trunk of a tree. If the average force exerted on the straw by the tree was 80 N, what was the speed of the straw when it hit the tree? 84.9 m/s

[Answer]

The force exerted on the straw to slow the straw to rest.

The average acceleration of the straw is   a = F/m = 80/0.60e-3 = 1.33e5m/s2

The distance traveled the straw; S = vi2/2a = 2.7e-2m

vi = sqrt (2 * a * S) = sqrt ( 2 * 1.33e5 * 2.7e-2) = 84.9 m/s

4. Walker3 7.P.054. [549638] Show Details The water skier in Figure 7-16 is at an angle of 34° with respect to the center line of the boat, and is being pulled at a constant speed of 14 m/s.

Figure 7-16

(a) If the tension in the tow rope is 94.0 N, how much work does the rope do on the skier in 10.0 s? 10.9 kJ (b) How much work does the resistive force of water do on the skier in the same time? -10.9 kJ

[Answer]

- Work  W = F * ΔX * cos(angle) = 94.0 * (14.0*10.0) * cos (34°) = 10.9 kJ

- W = Δ K = 0 = Wrope + Wresist (  Wresist = -10.9 kJ

5. Walker3 7.P.058. [549613] Show Details The force shown in Figure 7-17 acts on an object that moves along the x axis.

Figure 7-17

(a) How much work is done by the force as the object moves from x = 0 to x = 2.2 m? 1.08 J (b) How much work is done by the force as the object moves from x = 0.6 m to x = 4.0 m? 1.5 J (c) How much work is done by the force as the object moves from x = 2.0 m to x = 3.7 m?0.626 J

[Answer]

Work = area underneath

- 1.08 J

- 1.5 J

- 0.626 J

6. Walker3 7.P.060. [549595] Show Details The motor of a ski boat produces a power of 36,600 W to maintain a constant speed of 15.0 m/s. To pull a water skier at the same constant speed, the motor must produce a power of 38000 W. What is the tension in the rope pulling the skier? 93.3 N

[Answer]

<variables referred here are all scalar: the magnitudes)

The extra power is to keep the skier in constant speed.

W =  (Presist + Pextra) *Δ t =Δ K = 0 (

Presist= Fr * V * cos (angle) = - Pextra = -(38000-36600) = -1400W

Fr = 93.3 N

The skier is in constant velocity motion (  T - Fr = 0 ( T = 93.3 N

7. Walker3 7.P.061. [549618] Show Details To make a batch of cookies you mix half a bag of chocolate chips into a bowl of cookie dough, exerting a 21.5 N force on the stirring spoon. Assume that your force is always in the direction of motion of the spoon.

(a) What power is needed to move the spoon at a speed of 0.27 m/s? 5.81 W
(b) How much work do you do if you stir the mixture for 2.0 min? 0.697 kJ

[Answer]

- P = F * V * cos(angle) = 21.5 * 0.27 * cos(0) = 5.81 W

- W = P *Δ t = 5.81 * 2*60 = 697 J = 0.697 kJ

8. Walker3 7.P.063. [549599] Show Details A catapult launcher on an aircraft carrier accelerates a jet from rest to 71.9 m/s. The work done by the catapult during the launch is 6.5  107 J.  (a) What is the mass of the jet? 25100 kg (b) If the jet is in contact with the catapult for 2.7 s, what is the power output of the catapult? 24.1 MW

[Answer]

- W =Δ K = Kf = 1/2 m v2  ( m = 2*W/v2 = 25100kg

- P = W/Δt = 6.5e7 / 2.7 = 2.41e7 W = 24.1 Mw

9. Walker3 7.P.065. [549636] Show Details A 1440 kg car delivers a constant 46.3 hp to the drive wheels. We assume the car is traveling on a level road and that all frictional forces may be ignored. (a) What is the acceleration of this car when its speed is 14.9 m/s?1.61 m/s2 (b) If the speed of the car is cut in half does its acceleration increase, decrease, or stay the same? increases (c) Calculate the car's acceleration when its speed is 26.6 m/s. 0.902 m/s2

[Answer]

(a) P = F * V *cos (angle) , when angle = 0, ( P = F * V ( F = P/V = m a

( a = P/V/a = 46.3*746/14.9/1440 = 1.61m/s2

(b) increases, since a is inverse proportional to V

(c) a = 46.3*746/26.6/1440 = 0.902 m/s2

10. Walker3 7.P.068. [549633] Show Details Two springs, with force constants k1 and k2 are connected in series, as shown in Figure 7-21. How much work is required to stretch this system a distance x from the equilibrium position?

Figure 7-21

(Use k1 for k1, k2 for k2, and x as necessary.)  (k1 k2 x^2) / (2*(k1+k2))

[Answer]

Tension force in spring 1 and 2 is the same

T = k1Δx1 = k2Δx2

x =Δx1+Δx2

Therefore

k1 x = (k1+k2 ) Δx2 (Δx2 = k1x/( k1+k2 )

k2 x = (k1+k2 ) Δx1 (Δx1 = k2x/( k1+k2 )

The change in potential energy (ignore the gravitational potential energy)

ΔP= 1/2 k1Δx12 + 1/2 k2Δx22 = k1*k2 * x2 / 2(k1+k2)

The required the work is then

W =ΔP = k1*k2 * x2 / 2(k1+k2)

11. Walker3 7.P.070. [549622] Show Details A block rests on a horizontal, frictionless surface. A string is attached to the block, and is pulled with a force of 45.0 N at an angle  above the horizontal, as shown in Figure 7-23. After the block is pulled through a distance of 1.50 m its speed is v = 2.60 m/s, and 45.0 J of work has been done on it.

Figure 7-23

(a) What is the angle ? 48.2° (b) What is the mass of the block? 13.3 kg

[Answer]

- W = F * Δx * cos () = 45.0 * 1.50 * cos  = 45.0J

Thus,  = arcos ( 45.0/45.0/1.50) = 48.2

- W = ΔK=1/2mvf2 ( m = 2*W/vf2

(  m = 13.3 kg

# Comments

end qcontentcontainer

end qcontainer

end qcontentcontainer

end qcontainer

end qcontentcontainer

end qcontainer

end qcontentcontainer

end qcontainer

end qcontentcontainer

end qcontainer

end qcontentcontainer

end qcontainer

end qcontentcontainer

end qcontainer

end qcontentcontainer

end qcontainer

end qcontentcontainer

end qcontainer

end qcontentcontainer

end qcontainer