Lab #1				Specific Heat of Metal

Goal: Measure specific heat of metal using calorimetric equation learned in the lecture.

Apparatus and Materials:  Water, heater, calorimeter, cups, temperature sensor, balance, scientific workshop interface, iMac.

Theory: According to the calorimetric theory, for components in an isolated system, heat_flow_in  = Heat_floww_out.  In this lab,

Mmetal Cmetal(Tmetal,initial – Tfinal ) = (Mw Cw  +  Mcup Ccup + Mstir Cstir)( Tfinal – Tinitial )

Solve the above equation to find Cmetal.

Cmetal=( Mw Cw  +  Mcup Ccup + Mstir Cstir)( Tfinal – Tinitial )/Mmetal/((Tmetal,initial – T,final )

Procedure:

- Measure the mass of empty calorimeter and stirrer (Mcup,Mstir) .

- Fill up the calorimeter with cold water (1/3 filled) and measure the total mass.

- Calculate the mass of cold water.

- Use data studio and sensors to measure the temperature of cold water (Tcold).

- Boil the water and record the temperature (Thot).

- Add hot water into the calorimeter and record the temperature (Tfinal).

- Measure the mass of calorimeter with its contents

- Calculate the mass of the hot water added (Mhot) .

Data Table

Mcup+Mstir		Mcold		Mhot		Tcold		Thot		Tfinal