P17 Problem 1.1

- Show that the NOR gate is universal.

- Show that the 2-to-1 multiplexer is universal.

- Is there any other two-input element, besides NAND and NOR, that is universal?

Answer to d. Show how to build AND, OR, and NOT gate from NOR gate.

Answer to e. Show how to build AND, OR, and NOT gate from 2-to-1 multiplexer.

Answer to f.  Yes,

P17 Problem 1.5 BCD-to-7segment decoder

- Inputs are BCD digits; the digits 6, 7, and 9 are displayed with 6, 3, and 6 segments.

Answer:

Circuit diagram:

P18  Problem 1.10

Prove that the following pairs of logic expressions are equivalent, first by truth table, and then by means of symbolic manipulation.

Proof:

Truth table:

| Input xyz | LHS | RHS |
| --- | --- | --- |
| 000 | 0 | 0 |
| 001 | 1 | 1 |
| 010 | 1 | 1 |
| 011 | 0 | 0 |
| 100 | 1 | 1 |
| 101 | 0 | 0 |
| 110 | 0 | 0 |
| 111 | 1 | 1 |

P18  Problem 1.10 d     Proof:

Truth table:

| Input wxyz | LHS | RHS |
| --- | --- | --- |
| 0000 | 0 | 0 |
| 0001 | 0 | 0 |
| 0010 | 1 | 1 |
| 0011 | 0 | 0 |
| 0100 | 0 | 0 |
| 0101 | 1 | 1 |
| 0110 | 1 | 1 |
| 0111 | 1 | 1 |
| 1000 | 1 | 1 |
| 1001 | 0 | 0 |
| 1010 | 1 | 1 |
| 1011 | 0 | 0 |
| 1100 | 1 | 1 |
| 1101 | 1 | 1 |
| 1110 | 0 | 0 |
| 1111 | 1 | 1 |

p.18  Problem 1.12

Assume x = (x2x1x0) two and (y2y1y0) two are 3-bit unsigned binary numbers. Write down a logic expression in terms of the six Booleans variables x2, x1, x0, y2, y1, and  y0 that assumes the value 1 iff:

- x = y

- x < y

- x ≤ y

Answer to a:

Answer to b:

Answer to c:

# Text boxes

| Input | Output |
| --- | --- |
| x3x2x1x0 | e6 | e5 | e4 | e3 | e2 | e1 | e0 |
| 0000 | 0 | 1 | 1 | 1 | 1 | 1 | 1 |
| 0001 | 0 | 0 | 0 | 0 | 1 | 1 | 0 |
| 0010 | 1 | 0 | 1 | 1 | 0 | 1 | 1 |
| 0011 | 1 | 0 | 0 | 1 | 1 | 1 | 1 |
| 0100 | 1 | 1 | 0 | 0 | 1 | 1 | 0 |
| 0101 | 1 | 1 | 0 | 1 | 1 | 0 | 1 |
| 0110 | 1 | 1 | 1 | 1 | 1 | 0 | 1 |
| 0111 | 0 | 0 | 0 | 1 | 1 | 1 | 1 |
| 1000 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| 1001 | 1 | 1 | 0 | 1 | 1 | 1 | 1 |

e6      x1x0

|  |  | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- | --- |
| x3x2 | 00 | 0 | 0 | 1 | 1 |
|  | 01 | 1 | 1 | 0 | 1 |
|  | 11 | x | x | x | x |
|  | 10 | 1 | 1 | x | x |

e5      x1x0

|  |  | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- | --- |
| x3x2 | 00 | 1 | 0 | 0 | 0 |
|  | 01 | 1 | 1 | 0 | 1 |
|  | 11 | x | x | x | x |
|  | 10 | 1 | 1 | x | x |

e4      x1x0

|  |  | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- | --- |
| x3x2 | 00 | 1 | 0 | 0 | 1 |
|  | 01 | 0 | 0 | 0 | 1 |
|  | 11 | x | x | x | x |
|  | 10 | 1 | 0 | x | x |

e3      x1x0

|  |  | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- | --- |
| x3x2 | 00 | 1 | 0 | 1 | 1 |
|  | 01 | 0 | 1 | 0 | 1 |
|  | 11 | x | x | x | x |
|  | 10 | 1 | 1 | x | x |

e2      x1x0

|  |  | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- | --- |
| x3x2 | 00 | 1 | 1 | 1 | 0 |
|  | 01 | 1 | 1 | 1 | 1 |
|  | 11 | x | x | x | x |
|  | 10 | 1 | 1 | x | x |

e1      x1x0

|  |  | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- | --- |
| x3x2 | 00 | 1 | 1 | 1 | 1 |
|  | 01 | 1 | 0 | 1 | 0 |
|  | 11 | x | x | x | x |
|  | 10 | 1 | 1 | x | x |

e0      x1x0

|  |  | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- | --- |
| x3x2 | 00 | 1 | 0 | 1 | 1 |
|  | 01 | 0 | 1 | 1 | 1 |
|  | 11 | x | x | x | x |
|  | 10 | 1 | 1 | x | x |

x3x2x1x0

e6

e5

e4

e3

e2

e1

e0